## Slide 1
Diabetic retinopathy (DR) is a leading cause of vision loss and blindness in working-age adults.
~640 Million people will have diabetes by 2040 and there are insufficient eye-care specialists to screen for DR.
Retinal photography is a well-validated approach for screening of DR but traditional cameras are expensive with limited portability.
An end-to-end point-of-care DR device may significantly improve accessibility and aid in screening for DR.
Combine easy, high quality smartphone-based retinal imaging with automated image analysis to detect referral-warranted DR (RWDR).
Compare automated grading vs expert human grading of DR from smartphone-based retinal photography.
72 diabetic patients undergoing routine dilated clinical exam were recruited from UM Kellogg Retina Clinic. 45 subjects were male, 27 were female, with a mean age of 56.7 ± 16.9 years. Of 144 eyes, 132 had evidence of DR by exam. Imaging was successfully performed in 121 eyes (23 eyes either had dense media opacity such as vitreous hemorrhage, or full imaging was deferred by patient)
Masked grading for DR and presence of clinically significant macular edema (CSME) was performed by two ophthalmologists in accordance with ETDRS modified Airlie House classification.
2B
3B
Comparison of automated and expert human grading of diabetic retinopathy
using smartphone-based retinal photography
Tyson N. Kim1, Patrick Li1, Leslie M. Niziol1, Malavika Bhaskaranand2, Sandeep Bhat2, Chaithanya Ramachandra2, Kaushal Solanki2, Jose Davila1 Frankie Myers3, Clay Reber3, David C. Musch1, Todd Margolis4, Daniel A. Fletcher3, Maria A. Woodward1, Yannis M. Paulus1
1University of Michigan Kellogg Eye Center, Ann Arbor, MI; 2EyeNuk Inc, Woodland, CA; 3University of California Berkeley Bioengineering, Berkeley, CA; 4Washington University, St. Louis, MO
INTRODUCTION
PURPOSE
METHODS
CONCLUSION
REFERENCES
Typical Good Imaging
Challenging Imaging
RESULTS
ACKNOWLEDGEMENTS
The Leiter Family Littlefield 2000 Trust
DISCLOSURES
TNK, FM, CR, TM, DAF are co-inventors of patented technology in CellScope Retina
MB, SB, CR, KS are co-inventors of patented technology used in EyeApp software
IOL Glare
Moderate Cataract
Imaging of Diabetic Retinopathy
Figure 7b: Imaging of diabetic retinopathy with CellScope Retina demonstrating retinal exudates, dot-blot hemorrhages, and epiretinal membrane with fibrovascular changes (left to right). Image quality is commonly reduced by reflection and glare from intraocular lens implant or media opacity.
Table 1: Eye-level and Patient-level sensitivity and specificity for referral-warranted diabetic retinopathy from CellScope Retina images using EyeApp and expert human grading. Referral-warranted diabetic retinopathy (RWDR) is defined as moderate to severe NPDR, PDR, and/or CSME. No RWDR is defined as none to mild NPDR without CSME.
Sensitivity and Specificity Analysis
CellScope Retina combined with EyeApp software achieves reasonable sensitivity and specificity in detection of RWDR at the person-level, with lower sensitivity but higher specificity than human graders.
Automated smartphone-based DR screening hold great promise toward improving accessibility of DR screening.
Additional study in the community with typical diabetic population is warranted.
RESULTS
Maamari, R.N., et al., A mobile phone-based retinal camera for portable wide field imaging. Br J Ophthalmol, 2014. 98(4): p. 438-41.
Bhaskaranand M, Ramachandra C, Bhat S, et al. Automated Diabetic Retinopathy Screening and Monitoring Using Retinal Fundus Image Analysis. Journal of Diabetes Science and Technology. 2016 10(2):254-261. doi:10.1177/1932296816628546.
Tufail A, Kepetanakis VV, Salas-Vega S, et al. An observational study to assess if automated diabetic retinopathy image assessment software can replace one or more steps of manual imaging grading and to determine their cost-effectiveness. Health Technol Assess. 2016 20(92):1-72
Bolster, N.M., M.E. Giardini, and A. Bastawrous, The Diabetic Retinopathy Screening Workflow: Potential for Smartphone Imaging. J Diabetes Sci Technol, 2016. 10(2): p. 318-24.
Garg, S.J., Applicability of Smartphone-Based Screening Programs. JAMA Ophthalmol, 2016. 134(2): p. 158-9
Woodward, M.A., et al., Telemedicine for ophthalmic consultation services: use of a portable device and layering information for graders. J Telemed Telecare, 2016
Techniques for scatter and local photocoagulation treatment of diabetic retinopathy: Early Treatment Diabetic Retinopathy Study Report no. 3. The Early Treatment Diabetic Retinopathy Study Research Group. Int Ophthalmol Clin, 1987. 27(4): p. 254-64
Grading diabetic retinopathy from stereoscopic color fundus photographs--an extension of the modified Airlie House classification. ETDRS report number 10. Early Treatment Diabetic Retinopathy Study Research Group. Ophthalmology, 1991. 98(5 Suppl): p. 786-806
Performance Analysis
Figure 9: Agreement in grading of DR severity compared with clinical exam. For grader 1, there was exact agreement in 50% of the eyes, and agreement within 1 step in 79.1% of the eyes (κ = 0.50, 95% CI, 0.39 – 0.61). Grader 1 was able to detect 93.9% of RWDR at the eye level (κ = 0.50, 95% CI, 0.41 – 0.60) and 96.2% at the patient level (κ = 0.44, 95% CI, 0.30 – 0.57). For grader 2, there was exact agreement in 54.6% of the eyes, and agreement within 1 step in 87% of the eyes (κ = 0.60, 95% CI, 0.49 – 0.71). Grader 2 was able to detect 88.8% of RWDR at the eye level (κ = 0.52, 95% CI, 0.43 – 0.61) and 92.3% at the patient level (κ = 0.43, 95% CI, 0.29 – 0.57). EyeApp software was able to detect 77.4% RWDR at the eye level (κ = 0.44, 95% CI, 0.35 – 0.52) and 93.9% at the patient level (κ = 0.69, 95% CI, 0.58 – 0.80).
Figure 1: Dilated fundus photographs are obtained with CellScope Retina, a smartphone-based retinal imaging system with automated multi-image acquisition (five 50 deg images comprise >100 deg montage). Optimized optics, multi-color illumination, integrated electronics, and external fixation display are controlled by app intelligence for easy, high quality imaging.
Figure 2: Images sent to the cloud for automated interpretation by EyeApp software for detection of referable-warranted diabetic retinopathy (RWDR, moderate NPDR or higher and/or CSME).
Grader 1
Grader 2
Figure 7a: Imaging of diabetic retinopathy with CellScope Retina demonstrating dot-blot and pre-retinal hemorrhages.
IOL Glare
KELLOGG EYE CENTER
MICHIGAN MEDICINE
#B0406
EYEAPP: SMARTPHONE-BASED AUTOMATED IMAGE ANALYSIS
Image Enhancement
Lesion Localization
Figure 5: Lesion detection. (A) Original image; (B) Green channel image with expert lesion annotations overlaid in red; (C) Green channel image with lesions identified by automated analysis overlaid in red. Saturation of red color in (C) indicates the confidence of the lesion classifier.
Enhanced Images
Original Images
Figure 3: Image enhancement ‘normalizes’ image appearance and improves lesion visibility
Quality Assessment
Figure 4: Automated quality assessment used to identify images with insufficient quality and exclude them from further analysis. Higher quality scores indicate better image quality.
Blink
Defocus
Original
Human
Automated
Figure 6: Flow diagram of EyeApp algorithm in determination of RWDR.
Glare
Figure 8: Receiver Operating Characteristic (ROC) curve of EyeApp software for RWDR detection in CellScope Retina images, obtained by plotting the true positive rates against the false positive rates at different operating (cut-off) points. Area under ROC curve = 0.87.
Chart: Percentage
| Grader 1 | Grader 2 | EyeApp
Perfect Agreement | 50 | 54.6
Within 1-step | 79 | 87
RWDR (eye) | 93.9 | 88.8 | 77.4
RWDR (patient) | 96.2 | 92.3 | 93.9
EyeApp
Notes: EyeApp produces a classification score for each patient which is thresholded at a given threshold value (cut-point) to provide a binary output of RWDR absent/present i.e. if the score >= threshold value, then output is RWDR present. The ROC curve is generated by gradually varying the cut-point and evaluating the percentage of true positives (Y-axis) and false positives (X-axis). For the sensitivity and specificity reported in Table 1, the cut-point was chosen to have high sensitivity and reasonable specificity.
EyeApp combines the lesion analysis information from all the images of a given patient/eye before providing the RWDR output for the patient/eye. Therefore, RWDR outputs are not present at image-level and hence we cannot say how many of those images had signs of RWDR.